## Slide 1: William Stallings Computer Organization and Architecture 9th Edition
Chapter 9
Computer Arithmetic

## Slide 2: Arithmetic & Logic Unit
Does the arithmetic and logical calculations on data
Everything else in the computer is there to service this unit
Based on the use of simple digital logic devices that can store binary digits and perform simple Boolean logic operations
E.g.:

## Slide 3: ALU Inputs and Outputs

## Slide 4: Review of Number Systems
How are numbers written
  Scratches on wall/rock
  Knots on a string
  Symbolically
Want to
  Represent a useful set of numbers
  Provide a unique way of representing a number
Most commonly used system
  Arabic numerals
  Positional representation
  Decimal (base 10)

## Slide 5: Decimal System (base 10)
Uses decimal digits (0, 1, …, 9)
Position of digit represents it’s magnitude
  836 = 8 x 102 + 3 x 10 + 6
Fractions use negative powers of 10
  0.313 = 3 x 10-1 + 1 x 10-2 + 3 x 10-3
The decimal number 472.256 would be

## Slide 6: Binary Number System (base 2)
Uses digits 0 and 1
Also positional
  1001.101 = 23 + 20 + 2-1 + 2-3 = 9.62510
You should be familiar with converting between binary and decimal
  If not, see kipirvine.com/asm/workbook/binhex.htm

## Slide 7: Hexadecimal Number System (base 16)
Uses digits 0, 1, 2, …, 9, A, B, C, D, E, F
Also positional
  300E.A07 = 3x163 + 14x160 + 10x16-1 +
  7x16-3 = 12302.6270898437510
You should also be familiar with converting between hex and decimal
  If not, see kipirvine.com/asm/workbook/binhex.htm
Note that 4 binary digits can be represented by 1 hexadecimal digit

## Slide 8: Decimal, Binary, and Hexadecimal

## Slide 9: Integer Representation
Only have 0 & 1 to represent everything
Positive numbers stored in binary
  e.g. 41=00101001
No minus sign
No period, or radix point
How are negative numbers represented?
  Sign-Magnitude
  Two’s complement
  One’s complement (not discussed in following)
One of great debates in 50s was about which format to use.

## Slide 10: Sign-Magnitude
Most significant bit is sign bit
0 means positive
1 means negative
+18 = 00010010
-18 = 10010010
Problems
  Need to consider both sign and magnitude in arithmetic
  Two representations of zero (+0 and -0)
Rarely used with integers today

## Slide 11: Two’s Complement
Most significant bit is sign bit
Positive integers represented in usual binary form
Negative integers use the following
  Take the Boolean complement of each bit of the corresponding positive integer
  Add 1 to the result
NOTE!! This is ONLY for negative values!
Only one representation of zero
Range using n bits is -2n-1 to 2n-1-1

## Slide 12: Two’s Complement Examples
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101

## Slide 13: Geometric Depiction of Twos Complement Integers

## Slide 14: Negation Special Case 1
0 = 00000000
Bitwise not 11111111
Add 1 to LSB +1
Result 1 00000000
Overflow is ignored, so:
- 0 = 0 

## Slide 15: Negation Special Case 2
-128 = 10000000
bitwise not 01111111
Add 1 to LSB +1
Result 10000000
So:
-(-128) = -128 Χ
Monitor MSB (sign bit)
It should change during negation

## Slide 16: Range of Numbers
8 bit 2s complement
  +127 = 01111111 = 27 -1
  -128 = 10000000 = -27
16 bit 2s complement
  +32767 = 011111111 11111111 = 215 - 1
  -32768 = 100000000 00000000 = -215

## Slide 17: Conversion Between Lengths
Positive number pack with leading zeros
+18 = 00010010
+18 = 00000000 00010010
Negative numbers pack with leading ones
-18 = 10010010
-18 = 11111111 10010010
i.e. pack with MSB (sign bit)

## Slide 18: Addition and Subtraction
Normal binary addition
Monitor sign bit for overflow
Take twos complement of subtrahend and add to minuend
  i.e. a - b = a + (-b)
So we only need addition and complement circuits

## Slide 19: Hardware for Addition and Subtraction

## Slide 20: Hardware Implementation of Unsigned Binary Multiplication

## Slide 21: Booth’s Algorithm

## Slide 22: Examples Using Booth’s Algorithm

## Slide 23: Flowchart for Unsigned Binary Division

## Slide 24: Real Numbers
Numbers with fractions
Could be done in pure binary
  1001.1010 = 24 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
  Very limited
  Has been used for decimal arithmetic
Moving?
  How do you show where it is?
  Use representation similar to scientific notation

## Slide 25: Typical 32-Bit Floating-Point Format

## Slide 26: Floating Point representation
Exponent is in excess or biased notation
  e.g. Excess (bias) 127 means
  8 bit exponent field
  Pure value range 0-255
  Subtract 127 to get correct value
  Range -127 to +128
Why is excess/bias needed?
  Think of the representation of 0.0 and 1.0

## Slide 27: Normalization
FP numbers are usually normalized
  i.e., exponent is adjusted so that leading bit (MSB) of mantissa is 1
Since it is always 1 there is no need to store it
  Referred to as the hidden bit
Compare this with scientific notation where numbers are normalized to give a single digit before the decimal point, e.g. 3.123 x 103

## Slide 28: FP Ranges
For a 32 bit number
  8 bit exponent
  +/- 2128  3.4 x 1038
Accuracy
  The effect of changing least significant bit (lsb) of mantissa
  23 bit mantissa 2-23  1.2 x 10-7
  About 7 decimal places

## Slide 29: Expressible Numbers

## Slide 30: IEEE 754
Standard for floating point storage
32 and 64 bit standards
8 and 11 bit exponent respectively
Extended formats (both mantissa and exponent) for intermediate results

## Slide 31: IEEE 754 Formats

## Slide 32: FP Arithmetic +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result

## Slide 33: Floating-Point Addition and Subtraction

## Slide 34: Floating-Point Multiplication

## Slide 35: Floating-Point Division